## Slide 1: DRIVER ACTION RECOGNITION USING ARTIFICIAL INTELLIGENCE
Name: Philip Lee Hann Yung
(U1923382D)
Supervisor: Assoc Prof Yap Kim Hui
Examiner: Prof Wen Changyun
Date: 9 May 2023
School of Electrical and Electronic Engineering

## Slide 2: Agenda
Background
Literature Review
Methodology
results
Conclusion

## Slide 3: Motivation
Background

## Slide 4: Distracted Driving
Distracted Driving
Background
Any activity that diverts attention from driving
[1] DISTRACTED DRIVERS #1 Crashing while using a Phone || Dash Cam Compilation, (Jun. 11, 2019). Accessed: Apr. 12, 2023. [Online Video]. Available: https://www.youtube.com/watch?v=_pccGggeW7Y
[2] “Distracted Driving | NHTSA.” https://www.nhtsa.gov/risky-driving/distracted-driving (accessed Oct. 32, 2022).
[3] National Center for Statistics and Analysis, Distracted Driving 2019, (Research Note. Report No. DOT HS 813 111). National Highway Traffic Safety Administration, 2021.
2019 US: 1162 injured + 9 killed / day
Reduce distracted driving!
Solution: Cabin Monitoring

## Slide 5: Real-world Implications
Cabin-monitoring system
  May be mandated for truck/bus drivers
  Safety for road users
E.g. Using mobile phone earlier!
Background

## Slide 6: Objective & Scope
Train deep learning-based models which can recognize driver’s actions in a car cabin environment.
  Robust, Real-time, Action after is out-of-scope
Background
Survey datasets and models
Train and evaluate models
Improve model robustness
Construct dataset and fine-tune

## Slide 7: Literature Review

## Slide 8: Video Action Recognition
Literature Review
[5] Y. Zhu et al., “A Comprehensive Study of Deep Video Action Recognition.” arXiv, Dec. 11, 2020. doi: 10.48550/arXiv.2012.06567.
Hand-crafted features
Two-stream networks
3D-CNNs
Efficient video modelling
2015 3D-CNNs
2017 Kinetics400 Inflated-3D ConvNet (I3D)
2019 Temporal Shift Module (TSM)
Requires: Spatio-temporal modelling capability

## Slide 9: Video Swin Transformer (VST)
2019 Temporal Shift Module (TSM)
[6] Z. Liu et al., “Video Swin Transformer,” in 2022 IEEE/CVF Conference on Computer Vision and Pattern Recognition (CVPR), Jun. 2022, pp. 3192–3201. doi: 10.1109/CVPR52688.2022.00320.
2015 3D-CNNs
2017 Kinetics400 Inflated-3D ConvNet (I3D)
2022 Video Swin Transformer (VST)
Literature Review

## Slide 10: Temporal Shift Module (TSM)
Main Idea:
Shift along temporal dimension to exchange information.
Must not harm spatial feature learning capability.
Literature Review
[7] J. Lin, C. Gan, and S. Han, “TSM: Temporal Shift Module for Efficient Video Understanding,” in 2019 IEEE/CVF International Conference on Computer Vision (ICCV), Oct. 2019, pp. 7082–7092. doi: 10.1109/ICCV.2019.00718
Enjoys 2D-CNN efficiencies
Optimised hardware implementation
Availability of pretrained weights

## Slide 11: Dataset
Drive&Act (DAA), 2019
Multi-modal, multi-view
83 activity labels (3 levels)
3 train-val-test splits
15 participants for variability
Largest dataset: 9.6m frames!
(in car-cabin activity domain)
TICaM: A Time-of-flight In-car Cabin Monitoring (123k frames)
Literature Review
[8] M. Martin et al., “Drive&Act: A Multi-Modal Dataset for Fine-Grained Driver Behavior Recognition in Autonomous Vehicles,” in 2019 IEEE/CVF International Conference on Computer Vision (ICCV), Oct. 2019, pp. 2801–2810. doi: 10.1109/ICCV.2019.00289

## Slide 12: Metric
BalAcc Score
Mean class accuracy
Class imbalance issue
Literature Review

## Slide 13: Single-modality
Methodology, Results

## Slide 14: End-to-end ML Project Pipeline
Methodology
Dataset
Drive&Act
Conti-Action-2023
Pre-processing
Video  Raw frames
Normalisation
Resize and Crop
① Train
3 model families
(TSM, I3D, VST)
③ Evaluate
Validation and testing sets
(BalAcc score)
Live Real-time System
Fine-tune on Conti-Action-2023
30 FPS Live System
② Fine-tune
Hyperparameters
④ Improve
Class imbalance mitigation
Multi-modal fusion
[9] “Machine Learning Pipeline - Javatpoint,” www.javatpoint.com. https://www.javatpoint.com/machine-learning-pipeline (accessed May 08, 2023).

## Slide 15: ① Training
3 model families
  TSM (main method)
  I3D
  VST
2 datasets
  Drive&Act (benchmark)
  Conti-Action-2023 (demo only)
Methodology
Efficient Models
NIR Videos
Research Gap!
TSM
Drive & Act

## Slide 16: ② Varying Learning Rate
Methodology
Sample BalAcc curve for selecting learning rate hyperparameter

## Slide 17: ② Fine-tune Hyperparameters
Methodology
Training Parameter | TSM | I3D | VST
(No. of Frames) Backbone Pretrained Weights Batch Size Number of Epochs Learning Rate LR Scheduler Optimizer | 8, 16 ResNet50 ImageNet/Kinetics400 32, 16 25 0.0010, 0.0005 Step decay: 9, 17 SGD | 32 ResNet50 Kinetics400 128 20 0.1000 Step decay: 9, 16 SGD | 32 VST: Tiny, Base Kinetics400 32, 16 20 0.0004 Cosine annealing AdamW
Training Parameter | TSM | I3D | VST
 | 8, 16 ResNet50 ImageNet/Kinetics400 32, 16 25 0.0010, 0.0005 Step decay: 9, 17 SGD | 32 ResNet50 Kinetics400 128 20 0.1000 Step decay: 9, 16 SGD | 32 VST: Tiny, Base Kinetics400 32, 16 20 0.0004 Cosine annealing AdamW
Loss function: Cross-entropy loss

## Slide 18: ③ Evaluation Methodology
Methodology
Spatial Crop
DAA Benchmarking
Fair, unbiased comparison!

## Slide 19: ④ Class Imbalance Mitigation
Class Weighting
Uniform Class Sampling
Hard Sample Mining
CW + HSM
Methodology
Modified cross-entropy loss function

## Slide 20: Results: Single Modality
TSM is recommended for real-time use applications!
Results
Model | Ns | Val ↑ | Test ↑ | Latency ↓ | Throughput ↑
I3D | 32 | 63.29 | 60.41 | 18.3 ms | 54.7 clips/s
TSM | 8 | 68.47 | 62.34 | 15.0 ms | 66.7 clips/s
VST: Tiny | 32 | 68.67 | 60.10 | 40.2 ms | 24.9 clips/s
VST: Base | 32 | 70.06 | 63.48 | 89.3 ms | 11.2 clips/s
Results are best from each model family, training procedure already includes class imbalance mitigation techniques.
TSM: CW+HSM I3D, VST: Uniform Class Sampling

## Slide 21: Results: Single Modality
Results
TSM: Base to CW+HSM
22 out of 34 classes ↑
(60.17  68.47)

## Slide 22: Results: Single Modality
Results

## Slide 23: Multi-modality
Methodology, Results

## Slide 24: ④ Multi-modality Fusion
Methodology
1 architecture
3 proposed architectures

## Slide 25: Results: Multi-modality
Results
Fusion Method | Modality | Val ↑ | Test ↑
No Fusion (single modality) |  | 70.35 69.33 68.31 | 62.72 59.81 58.28
Late Fusion: Type C (linear weighted scores) |  | 71.47 74.06 74.02 75.20 | 64.99 65.09 63.24 66.32
Fusion Method | Modality | Val ↑ | Test ↑
No Fusion (single modality) |  | 70.35 69.33 68.31 | 62.72 59.81 58.28
Late Fusion: Type C (linear weighted scores) |  | 71.47 74.06 74.02 75.20 | 64.99 65.09 63.24 66.32
Fusion using TSM model, only best fusion method is shown.

## Slide 26: Results: Multi-modality
Results

## Slide 27: Live real-time System
Methodology, Results

## Slide 28: Conti-Action-2023
15 volunteers
32 classes
Day and night scenes
Camera position:
  Center of Dashboard
Methodology

## Slide 29: System Optimizations
Right crop then square crop
Data transformations
  94.1 ms  15.6 ms
  6 times improvement
Methodology

## Slide 30: Results: Live Real-time Prototype
Results

## Slide 31: Results: Demo Videos
Results
Local webpage for self-exploration

## Slide 32: Conclusion

## Slide 33: Conclusion
Drive&Act (DAA)
1. Fine-tune and benchmark 3 model families on accuracy and efficiency
Internal Dataset
3. Data construction and annotation
2. Model robustness improvement: (a) Class imbalance mitigation (b) Multi-modality fusion techniques
4. Live, real-time prototype system
Conclusion
TSM, I3D, VST

## Slide 34: Future Work
More extensive dataset
Advanced multi-modality fusion techniques
  Continuation of FYP
Conclusion

## Slide 35: Thank you!
QnA

## Slide 36: Appendix

## Slide 37: Background
The number of fatalities in distraction-affected crashes, i.e., a crash involving at least one driver who was distracted, was 3,522, or 8.2 percent of total fatalities in 2021. This represents a 12-percent increase from 3,154 in 2020.
3522 / 365 = 9.65 people per year
https://www.nhtsa.gov/risky-driving/distracted-driving
https://crashstats.nhtsa.dot.gov/Api/Public/ViewPublication/813435
Appendix

## Slide 38: Kinetics400 Dataset
Realistic action videos
Collected from YouTube
306,245 short trimmed videos
400 action categories
Appendix
W. Kay et al., “The Kinetics Human Action Video Dataset.” arXiv, May 19, 2017. doi: 10.48550/arXiv.1705.06950.

## Slide 39: Balanced Accuracy Score
Appendix
BalAcc Score
Mean class accuracy
Class imbalance issue

## Slide 40: VST Architecture
For the VST model, there are four variants officially released – tiny, small, base, and large. The variants differs in two ways: (i) the hidden channel number in the first stage (ii) the number of VST blocks in the third stage.
Appendix
Z. Liu et al., “Video Swin Transformer,” in 2022 IEEE/CVF Conference on Computer Vision and Pattern Recognition (CVPR), Jun. 2022, pp. 3192–3201. doi: 10.1109/CVPR52688.2022.00320.

## Slide 41: ResNet50 + TSM Architecture
Appendix
K. He, X. Zhang, S. Ren, and J. Sun, “Deep Residual Learning for Image Recognition.” arXiv, Dec. 10, 2015. doi: 10.48550/arXiv.1512.03385.
Temporal Shift Module added here

## Slide 42: ResNet50 Architecture
Appendix
K. He, X. Zhang, S. Ren, and J. Sun, “Deep Residual Learning for Image Recognition.” arXiv, Dec. 10, 2015. doi: 10.48550/arXiv.1512.03385.

## Slide 43: Optimizer: SGD
Appendix
https://www.analyticsvidhya.com/blog/2022/07/gradient-descent-and-its-types/

## Slide 44: LR Schedulers
Appendix
I. Loshchilov and F. Hutter, “SGDR: Stochastic Gradient Descent with Warm Restarts.” arXiv, May 03, 2017. doi: 10.48550/arXiv.1608.03983.

## Slide 45: Data Transformation Pipeline
Appendix

## Slide 46: DAA Setup
Appendix

## Slide 47: DAA Statistics
Appendix

## Slide 48: DAA Splits
Appendix

## Slide 49: Effect of Learning Rate Scheduler
Appendix

## Slide 50: Results: TSM Single Modality
Appendix

## Slide 51: Results: Single Modality
Appendix

## Slide 52: Results: Single Modality
Appendix

## Slide 53: Multi-Modality Fusion
Appendix

## Slide 54: Late Fusion Type C
Appendix

## Slide 55: Results: Multi-Modality
Appendix

## Slide 56: Results: Multi-Modality
Appendix

## Slide 57: Optimized Data Transformation
Appendix

## Slide 58: Sliding Temporal Window
Appendix
GeForce RTX 3080 GPU card
, Number of frames
, Step size

## Slide 59: Live Real-time: Latency Profiles
Appendix

## Slide 60: Full Results: Live Real-time Prototype
Appendix

## Slide 61: Conclusion
Improved accuracies
  Baseline to CW+HSM: 8 BalAcc points increase
  Single modality to multi-modality: 5 BalAcc points increase
30 FPS live prototype
  Low latency and high accuracy
Appendix